## Slide 1: Brick
A fired clay masonry product.

## Slide 2: Face Brick
Brick that is uniform in size and has sharp corners and lines.

## Slide 3: Ashlar stonework
Stonework that uses dressed, cut, or squared stones to provide a regular pattern or finished appearance.

## Slide 4: Coursed Rubble
Rubble stonework in which all of the stones are generally flat or rectangular, so that the result looks like courses (rows) of stone.

## Slide 5: Rubble Stonework
Stonework made up of undresses stones of irregular shapes.

## Slide 6: Masonry wall
A wall constructed entirely of brick, concrete block, stone, clay tile, terra cotta, or a combination of these materials.

## Slide 7: Insulated concrete forms (ICFs)
Concrete wall forms made of foam insulation that are filled with concrete and remain in place to become part of the exterior wall structure.

## Slide 8: Exterior insulation finish system (EIFS):
A wall covering system that provides thermal insulation and a durable external finish resembling stucco or stone.

## Slide 9: Stucco
A coating applied to the outside of a structure that forms a protective, low maintenance, yet decorative shell around the structure; consist of Portland cement, lime, sand, and water.

## Slide 10: Scratch Coat
The first stucco layer in the three-coat stucco system, which covers the lath and provides support for the second coat.

## Slide 11: Brown coat
The second stucco layer in the three-coat process; covers any lath not covered by the scratch coat, adds strength to the shell, trues up the surface, and provides an appropriate surface for the final coat.

## Slide 12: Brown coat
The second stucco layer in the three-coat process; covers any lath not covered by the scratch coat, adds strength to the shell, trues up the surface, and provides an appropriate surface for the final coat.

## Slide 13: Finish Coat
The third stucco layer in the three-coat process; a thin layer in which texture or design patterns are applied.

## Slide 14: Lath
A wire or ribbed material that provides support and attachment for the layers of stucco applied to a wall.

## Slide 15: Moisture barrier
A membrane places under a stucco finish that protects most of the wall area from moisture accumulation between the structure and the stucco.

## Slide 16: Firecut
An angles cut on a joist end in solid brick and stone walls to prevent toppling the wall if the house should catch fire.

## Slide 17: Cripple stud
A structural member, also called a jack stud that is not full length due to a wall opening.

## Slide 18: Furring strip
Strips of 2x2 or 1x3 lumber affixed to a masonry wall to provide a nailing surface for drywall, plaster, or paneling.

## Slide 19: Header- and- Stud framing
A method of constructing headers for window and door opening in which shorter studs and jack studs are firmly nailed to the sole and top of the opening.

## Slide 20: Jack stud
A structural member positioned inside a wall opening to help support the header over the opening.

## Slide 21: Sole plate
The bottom horizontal member of a frame wall, on which the studs rest.

## Slide 22: Elevation
A drawing, typically made as an orthographic projection, that shows the exterior features of one side of a structure

## Slide 23: Grade Line
The line or level of the finished grade (earth) around the structure.